## Slide 1: NAVIO 2 드론 제작
2019년 6월 9일
성병문
한세대학교 자율 비행

## Slide 2: NAVIO 개요

## Slide 3: NAVIO2
홈페이지
  https://emlid.com/navio/
  https://docs.emlid.com/navio2/

## Slide 4: NAVIO2 특징
가격 : 25만원
GNSS receiver
  Tracks GPS, GLONASS, Beidou, Galileo and SBAS satellites. External antenna with MCX connector
Dual IMU
  Accelerometers, gyroscopes and magnetometers for orientation and motion sensing
RC I/O co-processor
  Accepts PPM/SBUS input and provides 14 PWM output channels for motors and servos
High resolution barometer
  Senses altitude with 10 cm resolution
Extension ports
  Exposed ADC, I2C and UART interfaces for sensors and radios
Triple redundant power supply
  With overvoltage protection and power module port for voltage and current sensing

## Slide 5: NAVIO OS 설치
This is a Raspbian you know with ArduPilot and ROS preinstalled and ready to run with a couple of simple commands. Also comes with DroneKit and GStreamer

## Slide 6: NAVIO 조립
조립

## Slide 7: NAVIO2 조립
홈페이지
  https://docs.emlid.com/navio2/
Powering Navio2 Attention
  ALL POWER SOURCES SHOULD PROVIDE VOLTAGE IN 4.8-5.3V RANGE, OTHERWISE YOU CAN DAMAGE YOUR NAVIO2 AND RASPBERRY PI.**
Navio2 has three power sources, all of them can be used simultaneously as they are protected by ideal diodes.

## Slide 8: 파워 공급
Navio2 should be powered by a power module connected to the “POWER” port on Navio2.
Navio2 will provide power to the Raspberry Pi.

## Slide 9: GPS 연결

## Slide 10: RC input
Navio2 supports PPM and SBUS signals as an RC input.
To connect receivers that do not support PPM output you can use PPM encoder.
PPM receiver is powered by Navio2 and does not require power on the servo rail.

## Slide 11: ESC 연결
ESCs are connected to RC outputs labeled from 1 to 14 on a 2.54mm header.
Only one ESC power wire (central) should be connected to Navio2 servo rail, otherwise BECs built in ESCs will heat each other.

## Slide 12: Servo 연결
Servos are connected to RC outputs labeled from 1 to 14 on a 2.54mm header.
Power module does not provide power to servos. To provide power to servos connect BEC to the servo rail. BEC would also serve as back-up power supply to Navio2.

## Slide 13: Telemetry Modem
UART radio
  For UART port use /dev/ttyAMA0 serial.
USB radio
  Use /dev/ttyUSB0 virtual serial port for USB.

## Slide 14: Barometer UV protection
MS5611 barometer (steel cap IC) is sensitive to UV light and might report sudden jumps in altitude under sunlight.
It is very important to cover it with a piece of open cell foam (something like microphone fabric) or put autopilot in a protective case to protect it both from sunlight and airstreams.

## Slide 15: Anti-vibration mount 1
We have designed an anti-vibration for Navio that can be easily 3D printed.
It significantly simplifies mounting and eliminates vibrations.

## Slide 16: Anti-vibration mount 2
STL Files
  Top
    https://github.com/emlid/hardware/blob/master/VibroNavio2top_rev_A.STL
  Bottom
    https://github.com/emlid/hardware/blob/master/VibroNavio2bot_rev_A.STL
You will also need 8 blue vibration damping balls from Hobbyking

## Slide 17: NAVIO 설정
조립

## Slide 18: 라즈비안 설치
기설정된 라즈비안 이미지 다운로드
  http://files.emlid.com/images/emlid-raspbian-20190227.img.xz

## Slide 19: GT-R530 NX

## Slide 20: GT-R530 NX
가격 : $ 200
F405 Flight Controller
Item Name: F405 Betaflight FC AIO OSD BEC
Input Power: 12.6 - 25V ( 3 - 6S )
BEC: 5V / 1.5A
MCU: STM32F405
Gyro: MPU6000, 8K Six-Axis
Max Lipo Cell: 3 – 5
FPV Transmitter
FPV Camera
Item Name: Runcam Micro Swift FPV
Camera
Image Sensor: 1/3 inch SONY Super HAD II Signal System: PAL / NTSC
S / N Ratio: more than 60dB ( AGC OFF )
Electronic Shutter Speed: PAL: 1 / 50 ~ 100,000; NTSC: 1 / 60 ~ 100,000
AutoGain Control ( AGC ): YES
Power: DC 5 to 36V

## Slide 21: NAVIO2 + GT-R530 드론 조립
구분 | 제품 | 모델/스펙 | 가격 | 수량
 | 모터/센서/본체 | GT - R530 NX | 23만원 | 1
 | 컴퓨터 | RASPBERRY PI B+ | 5 만원 | 1
 | 콘트롤러 | NAVIO2 | 20 만원 | 1
계 |  |  | 48 만원 | 

## Slide 22: NAVIO2 기반 드론 조립
콘트롤러
  NAVIO2 (10만원)
    https://emlid.com/navio/
본체
  GT-R530 NX( $ 243 )
    https://www.gearbest.com/brush-fpv-racer/pp_009542172048.html?wid=1433363
  SHRC H1G ($ 94)
    https://www.gearbest.com/rc-quadcopters/pp_009187953341.html?wid=1433363
  JDRC JD ($ 80)
    https://www.gearbest.com/rc-quadcopters/pp_009531904281.html?wid=1433363
  GEPRC Mark2 ($ 264)
    https://www.gearbest.com/brush-fpv-racer/pp_009166157856.html?wid=1433363
  Aurora RC Mini Fight ($ 137)
    https://www.gearbest.com/brushless-fpv-racer/pp_1156927.html?wid=1433363

## Slide 23: NAVIO2 드론 조립 예
https://community.emlid.com/t/first-build-quadcopter-autonomous-drone-rpi-3-b-navio2/12597

## Slide 24: 끝.