## Slide 1: NAVIO 2 드론 제작
2019년 6월 9일
성병문
한세대학교 자율 비행

## Slide 2: NAVIO 개요

## Slide 3: NAVIO2
홈페이지
  https://emlid.com/navio/
  https://docs.emlid.com/navio2/
What is NAVIO2?
  Autopilot HAT(Hardware Attached on Top) for Raspberry Pi
  Powered by ArduPilot and ROS
  Supports PX4
  $ 168
  Turn your Raspberry Pi® into a drone controller

## Slide 4: NAVIO2 특징
GNSS receiver
  Tracks GPS, GLONASS, Beidou, Galileo and SBAS satellites. External antenna with MCX connector
Dual IMU
  Accelerometers, gyroscopes and magnetometers for orientation and motion sensing
RC I/O co-processor
  Accepts PPM/SBUS input and provides 14 PWM output channels for motors and servos
High resolution barometer
  Senses altitude with 10 cm resolution
Extension ports
  Exposed ADC, I2C and UART interfaces for sensors and radios
Triple redundant power supply
  With overvoltage protection and power module port for voltage and current sensing

## Slide 5: NAVIO OS 설치
This is a Raspbian you know with ArduPilot and ROS preinstalled and ready to run with a couple of simple commands. Also comes with DroneKit and GStreamer

## Slide 6: NAVIO H/W 조립
조립

## Slide 7: NAVIO2 드론 조립 예
https://community.emlid.com/t/first-build-quadcopter-autonomous-drone-rpi-3-b-navio2/12597
https://www.instructables.com/id/Step-by-step-Guidance-to-Build-a-Drone-From-Scratc/

## Slide 8: NAVIO2 조립
홈페이지
  https://docs.emlid.com/navio2/
Powering Navio2 Attention
  ALL POWER SOURCES SHOULD PROVIDE VOLTAGE IN 4.8-5.3V RANGE, OTHERWISE YOU CAN DAMAGE YOUR NAVIO2 AND RASPBERRY PI.**
Navio2 has three power sources, all of them can be used simultaneously as they are protected by ideal diodes.

## Slide 9: 드론 Quadcopter NAVIO 조립

## Slide 10: Navio2 배선

## Slide 11: 파워 공급 1
Navio2 should be powered by a power module connected to the “POWER” port on Navio2.
Navio2 will provide power to the Raspberry Pi.

## Slide 12: 파워 공급 2

## Slide 13: GPS 연결

## Slide 14: ESC 연결
ESCs are connected to RC outputs labeled from 1 to 14 on a 2.54mm header.
Only one ESC power wire (central) should be connected to Navio2 servo rail, otherwise BECs built in ESCs will heat each other.

## Slide 15: Servo 연결
Servos are connected to RC outputs labeled from 1 to 14 on a 2.54mm header.
Power module does not provide power to servos. To provide power to servos connect BEC to the servo rail. BEC would also serve as back-up power supply to Navio2.

## Slide 16: RC input
PPM 과 SBUS 형식의 RC 입력 신호만을 지원한다.
PPM 타입 RC Controller
  Frsky Taranis
    https://www.frsky-rc.com/product/taranis-x9d-plus-2/

## Slide 17: FrSKY X8R과 Navio2 연결 예

## Slide 18: Telemetry Modem
UART radio
  For UART port use /dev/ttyAMA0 serial.

## Slide 19: Barometer UV protection
MS5611 barometer (steel cap IC) is sensitive to UV light and might report sudden jumps in altitude under sunlight.
It is very important to cover it with a piece of open cell foam (something like microphone fabric) or put autopilot in a protective case to protect it both from sunlight and airstreams.

## Slide 20: Anti-vibration mount 1
We have designed an anti-vibration for Navio that can be easily 3D printed.
It significantly simplifies mounting and eliminates vibrations.

## Slide 21: Anti-vibration mount 2
STL Files
  Top
    https://github.com/emlid/hardware/blob/master/VibroNavio2top_rev_A.STL
  Bottom
    https://github.com/emlid/hardware/blob/master/VibroNavio2bot_rev_A.STL
You will also need 8 blue vibration damping balls from Hobbyking
  https://hobbyking.com/en_us/vibration-damping-ball-65g-bag-of-8.html

## Slide 22: 라즈베리파이 케이스
https://www.thingiverse.com/thing:3712499?fbclid=IwAR0q23hTFudF2WR6drXF0MihutdcCVjp1nGQSJyXfh7dTh9L-Sk7-IEVzkE
https://www.thingiverse.com/thing:3714695?fbclid=IwAR2kpwI0rKJyGNhlsDpJ_Qi9enSqlocVV1SZ8qa6bXuRHgcDlFpWOtUVXCo

## Slide 23: NAVIO S/W 설치
조립

## Slide 24: 라즈비안 설치
기설정된 라즈비안 이미지 다운로드
  http://files.emlid.com/images/emlid-raspbian-20190227.img.xz

## Slide 25: 라즈비안 환경 설정
Wi-Fi 설정
  sudo vi /etc/wpa_supplicant/wpa_supplicant.conf
    network={
      ssid="yourssid"
      psk="yourpasskey"
    }
Expading rootfs
  sudo raspi-config --expand-rootfs

## Slide 26: Specifying launching options
Open the file:
  sudo nano /etc/default/arducopter
  sudo systemctl daemon-reload
Here you can specify IP of your ground station.

## Slide 27: Launching a custom ArduPilot binary
Navio is supported in ArduPilot upstream and if you'd like to build the binary yourself please proceed to the Building from sources.
  https://docs.emlid.com/navio2/common/ardupilot/building-from-sources/
Download arducopter binary
  wget --no-cache http://firmware.eu.ardupilot.org/Copter/stable/navio2/arducopter
  chmod +x arducopter

## Slide 28: Launching a custom ArduPilot binary 2
서비스 파일 /etc/systemd/system/ardupilot.service 을 편집한다.
[Unit]
Description=ArduPilot for Linux
After=systemd-modules-load.service
Documentation=https://docs.emlid.com/navio2/navio-ardupilot/installation-and-running/#autostarting-ardupilot-on-boot
Conflicts=arduplane.service arducopter.service ardurover.service
[Service]
EnvironmentFile=/etc/default/ardupilot
# Uncomment and modify this line if you want to launch your own binary
ExecStart=/bin/sh -c "/home/pi/arducopter ${ARDUPILOT_OPTS}"
##### CAUTION ######
# There should be only one uncommented ExecStart in this file
Restart=on-failure
[Install]
WantedBy=multi-user.target

## Slide 29: Launching a custom ArduPilot binary 3
ArduPilot 재시작
  sudo systemctl daemon-reload
  sudo systemctl status ardupilot
  sudo systemctl start ardupilot
  sudo systemctl enable ardupilot

## Slide 30: ardupilot 소스 빌딩
Python 패키지 설치
  pip install future
Aliasing
  alias waf="$PWD/modules/waf/waf-light"
Download the ArduPilot code and update submodules:
  git clone https://github.com/ArduPilot/ardupilot.git
  cd ardupilot
  git submodule update --init –recursive
Waf config
  waf configure --board=navio2
Build arducopter
  waf copter
Copy the binary
  cp build/navio2/bin/arducopter ~

## Slide 31: Video Streaming
문서
  https://docs.emlid.com/navio2/common/dev/video-streaming/

## Slide 32: PX4 소스 빌딩 1
문서
  https://docs.px4.io/en/flight_controller/raspberry_pi_navio2.html
Changing hostnames
Setting up Avahi (Zeroconf)
  sudo apt install avahi-daemon insserv
  sudo insserv avahi-daemon
  sudo apt-get install python-jinja2
  sudo pip install numpy toml

## Slide 33: PX4 소스 빌딩 2
폴더 이동
  cd ~/src/Firmware
소스 업데이트
  git pull
  git submodule sync --recursive
  git submodule update --init --recursive
빌드
  make emlid_navio2_native
실행
  cd ~/src/Firmware
  sudo killall arducopter
  sudo ./build/emlid_navio2_native/bin/px4 -s ./posix-configs/rpi/px4.config

## Slide 34: PX4 자동 실행
sudo vi /etc/rc.local
  systemctl stop arducopter
  cd /home/pi/src/Firmware && ./build/emlid_navio2_native/bin/px4 -d -s ./posix-configs/rpi/px4.config > px4.log

## Slide 35: RC 연결

## Slide 36: X8R Binding Procedure
Binding is the process of uniquely associating a particular receiver to a transmitter module. A transmitter module can be bound to multiple receivers (not to be used simultaneously). A receiver can only be bound to one transmitter module.
Follow the steps below to finish the binding procedure.
  Turn on the transmitter while holding the F/S button on the module (please refer to the module instruction manual for switch positions). Release the button. The RED LED on the XJT module will flash, indicating the transmitter is ready to bind to the receiver.
  Set X8R receiver in bind mode (see below chart for details), The RED LED on the receiver will flash, indicating the binding process is completed.
  Turn off both the transmitter and the receiver.
  Turn on the transmitter and connect the battery. The GREEN LED on the receiver indicates the receiver is receiving commands from the transmitter. The receiver/transmitter module binding will not have to be repeated, unless one of the two is replaced

## Slide 37: FrSky X8R 수신기 바인딩 1
바인딩 방법
  https://www.youtube.com/watch?v=RH_RuVbF2YU

## Slide 38: FrSky X8R 수신기 바인딩 2
바인딩 방법
  https://www.youtube.com/watch?v=jUkutJrzXFI

## Slide 39: X8R 수신기와 Navio 초기 연결
X8R 수신기와 Navio 초기 연결 모습
  바인딩 되지 않으면 수신기에 적색 LED가 깜빡 거림.

## Slide 40: X8R 수신기와 Navio 바인딩
X8R 수신기와 Navio 바인딩 결과
  바인딩 되지 않으면 수신기에 녹색 LED가 깜빡 거림.

## Slide 41: ArduPilot에서 RC 캘리브레이션
ArduPilot에서 RC 신호를 보정할 수 있음.

## Slide 42: GT-R530 NX

## Slide 43: GT-R530 NX
가격 : $ 200
F405 Flight Controller
Item Name: F405 Betaflight FC AIO OSD BEC
Input Power: 12.6 - 25V ( 3 - 6S )
BEC: 5V / 1.5A
MCU: STM32F405
Gyro: MPU6000, 8K Six-Axis
Max Lipo Cell: 3 – 5
FPV Transmitter
FPV Camera
Item Name: Runcam Micro Swift FPV
Camera
Image Sensor: 1/3 inch SONY Super HAD II Signal System: PAL / NTSC
S / N Ratio: more than 60dB ( AGC OFF )
Electronic Shutter Speed: PAL: 1 / 50 ~ 100,000; NTSC: 1 / 60 ~ 100,000
AutoGain Control ( AGC ): YES
Power: DC 5 to 36V

## Slide 44: NAVIO2 + GT-R530 드론 조립
구분 | 제품 | 모델/스펙 | 가격 | 수량
 | 모터/센서/본체 | GT - R530 NX | 23만원 | 1
 | 컴퓨터 | RASPBERRY PI B+ | 5 만원 | 1
 | 콘트롤러 | NAVIO2 | 20 만원 | 1
계 |  |  | 48 만원 | 

## Slide 45: NAVIO2 기반 드론 조립
콘트롤러
  NAVIO2 (10만원)
    https://emlid.com/navio/
본체
  GT-R530 NX( $ 243 )
    https://www.gearbest.com/brush-fpv-racer/pp_009542172048.html?wid=1433363
  SHRC H1G ($ 94)
    https://www.gearbest.com/rc-quadcopters/pp_009187953341.html?wid=1433363
  JDRC JD ($ 80)
    https://www.gearbest.com/rc-quadcopters/pp_009531904281.html?wid=1433363
  GEPRC Mark2 ($ 264)
    https://www.gearbest.com/brush-fpv-racer/pp_009166157856.html?wid=1433363
  Aurora RC Mini Fight ($ 137)
    https://www.gearbest.com/brushless-fpv-racer/pp_1156927.html?wid=1433363

## Slide 46: NAVIO2 드론 조립 예
https://community.emlid.com/t/first-build-quadcopter-autonomous-drone-rpi-3-b-navio2/12597

## Slide 47: 끝.